## Slide 1
Notes: Reference: teslamotors.com

## Slide 2: Game-changing features
Torque in AC induction motors
“Throttle” response time in EVs
Battery design and capacity
Safety
Limitations

## Slide 3: Torque
Notes: Reference: http://www.teslamotors.com/forum/forums/saleen-tesla-gear-ratio?page=1
Reference: http://www.motortrend.com/roadtests/alternative/1411_2015_tesla_model_s_p85d_first_test/

## Slide 4: “Throttle” response time
Notes: Reference: http://www.motortrend.com/roadtests/oneyear/alternative/1404_2013_tesla_model_s_p85_update_3/
Response time is nearly instant- makes the car feel like an extension of your body- very fun driving experience.
Electron fast throttle response time
More flexibility in component placement
  Low center of gravity
  Empty frunk for safety
Fast acceleration
Few moving parts

## Slide 5: Battery
~7000 Li-ion cells by Panasonic
BMS controls cells and balances charge.
Worst degradation is time held high and low SOC.
For normal use charge to 80% and life will be significantly longer. 100% max range setting for road trips.
  Can’t keep a Leaf between 20% and 80% without range anxiety.
~10 year life
Coolant system allow fast charging 150 miles in first 20 minutes. 1 hour for full charge.
Small cells individually fused for safety.
Cylindrical cells packing leaves a lot of empty space- allows deformation during accident decreases puncture and decreases load transfer.
Safety gel sprayed onto all cells. In a fire, the gel expands into a foam, sealing air gaps around dangerous cell, cuts off air supply- no air, no fire!
Battery system under car for low CG, even F-R weight distribution, and out of the way.
Notes: Reference: http://hackaday.com/2014/09/13/tesla-model-s-battery-teardown/
Battery is heavy ~800 lbs.
Chassis aluminum to minimize weight, but still too heavy:
Total Curb weight: 4,647.3 lbs
Battery pack under the car
  Low center of gravity
  Even front back weight distribution
  Clears up space under the hood as crumple zone

## Slide 6: Safety
Low CG, large foot-print, lots of empty space allows optimization for safety.
5-star NHTSA and NCAP safety rating.
Crash test video: https://www.youtube.com/watch?v=dz2FMfv-CSc
Notes: Reference: https://www.youtube.com/watch?v=dz2FMfv-CSc

## Slide 7: Limitations
Limited range and long charging time
  Supercharger- first 150 miles range in 20 minutes
  Battery-swapping
  Most trips are within the range of the car
Single gear limits top speed at 120 mph as motor can’t handle higher RPM
  Dual motor version: each motor is geared differently so it can go to 155 mph
Energy density of Li-ion battery much lower than gasoline not great for race cars
Tesla at the Nurburgring

## Slide 8: Pro
Fast response time
Instant torque
Low CG
Small component footprint
  400 hp motor the size of a water melon
  Empty frunk
Electronic controlled AWD easy
No transmission (single fixed gear. reverse current, reverse drive)
Few moving parts
Con
Long refueling time
Limited range
Low energy density of batteryheavy
Complex electronics needed to control battery
Cost
Not for race track
Notes: No more gas stations (especially nice in a snow storm)
No more oil changes, air filter changes, transmission fluid changes etc etc
Quieter roads
No emissions at the tailpipe- can be driven indoors
Regenerative breaking saves energy, and minimizes use of mechanical breaks- prolonging breakpad life and decreasing break dust.

## Slide 9
P85D first drive video: https://www.youtube.com/watch?v=JyxTey3ADAA
Notes: Reference: https://www.youtube.com/watch?v=JyxTey3ADAA

## Slide 10: Records and awards
Lowest CD production car when released (0.24).
Longest-range production EV.
Consumer Reports highest rating in their history 99/100.
MotorTrend Car of the Year 2013
Safest crash-tested car on the road (NHTSA when considering all subcategories).
P85D fastest accelerating 4 door sedan (0-60 in 3.1s). 691 hp.